## Slide 1: Hamming Code
It is an error detection and error correction code.
Data can be of any length.
No. of parity bit is decided by: 2^n

## Slide 2: Hamming Code
Positions for parity bits are decided by 2^n, where n can be 0,1,2….n.
2^0 = 1
2^1 = 2
2^2 = 4
2^3 = 8 and so on.

## Slide 3: Hamming Code
Parity Bits
 | P4 | P2 | P1
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
Example: Use 7 bit hamming code for error detection and correction. Use Even parity.
Data: 1001
Parity Bits = ? - > 3 (as data bits are 4)
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 0 | 0 |  | 1 |  | 
STEP 1
Now how we will calculate the parity bits? P1 -> D3 , D5 , D7 P2 -> D3, D6, D7
P3 -> D5, D6, D7
STEP 2
Calculating parity bits:
P1 | D3 | D5 | D7
0 | 1 | 0 | 1
Since, D3, D5 & D7 are already having even 1’s -> that’s why P1 is 0.

## Slide 4: Hamming Code
Parity Bits
 | P4 | P2 | P1
0 | 0 | 0 | 0
1 | 0 | 0 | 1
2 | 0 | 1 | 0
3 | 0 | 1 | 1
4 | 1 | 0 | 0
5 | 1 | 0 | 1
6 | 1 | 1 | 0
7 | 1 | 1 | 1
STEP 2
STEP 3
P4 | D5 | D6 | D7
1 | 0 | 0 | 1
P2 | D3 | D6 | D7
0 | 1 | 0 | 1
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 0 | 0 | 1 | 1 | 0 | 0
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 0 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1 | 0 | 0
Encoded Message

## Slide 5: Hamming Code: Following Even Parity
Intentionally Creating Error
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 1 | 0 | 1 | 1 | 0 | 0
Error Detection
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 1 | 0 | 1 | 1 | 0 | 0
Calculate Parity Again
P1 | D3 | D5 | D7
0 | 1 | 0 | 1
P2 | D3 | D6 | D7
0 | 1 | 1 | 1
P4 | D5 | D6 | D7
1 | 0 | 1 | 1
No of 1’s are not even, hence P1 will become 1.
This block is following the even parity rule, hence this is correct
No of 1’s are not even here as well, hence P4 will be 1.

## Slide 6: Hamming Code
Now write the parity bits separately:
P4 | P2 | P1
1 | 1 | 0
Decimal of 1 1 0 => 6 Means, there is a error in 6th bit. So if 6th bit is 0 then make it 1, or if it is 1 then make 0.
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 1 | 0 | 1 | 1 | 0 | 0
D7 | D6 | D5 | P4 | D3 | P2 | P1
1 | 0 | 0 | 1 | 1 | 0 | 0
Hence, Error is detected and corrected as well. Data Received is: 1001100