## Slide 1: Computer Networks
CSE-AIT Unit-02 Chapter 2.1
ALOK KUMAR – ASSISTANT PROFESSOR & KARGIL TECHINCAL TRAINER (DCPD) EMAIL: DCPD.KARGILT1@CUMAIL.IN

## Slide 2: Contents
Network Layer Design Issues & IP Addressing both Classful and Classless.
Subnetting and Supernetting.
Examples for Subnetting.
Forwarding of IP Packets.
IP Header and IPV4 and IPV6 Addressing.
Network Layer Protocols.

## Slide 3: Where does the Network Layer come in?
The Network Layer is Layer 3 of the OSI model.
Its major responsibility is: To deliver packets from the source device to the destination device across one or more interconnected networks.

## Slide 4: Network Layer Desing Issues / Responsibilities.
No. | Network Layer Responsibility / Design Issue | One-line Explanation
1 | Logical Addressing | Provides IP addresses to identify source and destination hosts/networks.
2 | Routing | Determines the best path through the network from source to destination.
3 | Forwarding | Sends a received packet through the correct outgoing interface toward its destination.
4 | Internetworking | Allows different networks to communicate and work together as one interconnected network.
5 | Packet Switching / Store-and-Forward | Routers receive, temporarily store, examine, and then forward packets.
6 | Connectionless / Datagram Service | Allows IP packets to be sent independently without establishing a connection first.

## Slide 5: Network Layer Desing Issues / Responsibilities.
7 | Connection-Oriented Service | Provides a logical path/connection before packets are transferred, as in virtual-circuit networks.
8 | Fragmentation and Reassembly | Handles packets that are larger than the MTU supported by a network.
9 | Congestion Control / Traffic Management | Helps prevent excessive traffic from overwhelming network resources.
10 | Quality of Service (QoS) | Helps provide suitable treatment to traffic with different requirements such as delay or bandwidth.

## Slide 6: 1. Logical Addressing
The Network Layer uses IP addresses to identify the source and destination of packets.
For example:
Suppose PC1 wants to send a packet to PC2.
The packet contains information such as:
The routers in between use the destination IP address to determine where the packet should go.
Why is this required?
A network may contain thousands or millions of devices.
The Network Layer needs a structured addressing system that tells routers: "Which network does this destination belong to?"
This is why IP addresses are divided conceptually into:
For example: 192.168.1.10 Network: 192.168.1.0
Host: 10

## Slide 7: 2. Routing
Routing is one of the most important responsibilities of the Network Layer.
Suppose we have:
PC1 wants to send a packet to PC2.
There are potentially multiple paths:
Path 1:PC1 → R1 → R2 → R4 → PC2 Path 2:PC1 → R1 → R3 → R4 → PC2
The router needs to determine: Which path should the packet take? This Process is called ROUTING

## Slide 8: 2. Routing
Routers use routing tables to make forwarding decisions.
For example:
Destination Network Next Hop
192.168.20.0/24 R2
192.168.30.0/24 R3
Routing protocols such as:
RIP
OSPF
EIGRP
BGP
can help routers learn routes

## Slide 9: 3. Forwarding
Routing and forwarding are related, but they are not the same thing.
Routing asks: "Which path should be used?"
Forwarding asks: "Where should I send this packet next?"
Suppose Router R1 receives: Destination IP: 192.168.20.10
Its routing table says:
R1 therefore forwards the packet through: G0/1
Conceptually:
If the destination is in Network B: Packet - > G0/1.

## Slide 10: 4. Internetworking
The word internetworking means connecting multiple independent networks so that devices on those networks can communicate.
For example:
These are two different IP networks.
Without Layer 3 routing, devices in Network A cannot directly communicate with devices in Network B.
The Network Layer provides the mechanisms that allow these different networks to communicate.
This is the basic idea behind an internetwork.

## Slide 11: 5. Packet Switching / Store-and-forward
At the Network Layer, data is carried in packets.
Consider: PC1 → R1 → R2 → R3 → PC2
When R1 receives a packet, it generally:
Step 1 — Receives the packet
PC1 ───────→ R1
Step 2 — Stores/buffers it
The router temporarily holds the packet.
Step 3 — Examines the packet
It examines the IP header, particularly information such as:
Source IP
Destination IP
TTL
Protocol
Step 4 — Makes a forwarding decision
The router checks its routing/forwarding information.
Step 5 — c
PC1 → R1 → R2
R2 performs a similar process.
This is called: Store-and-forward packet switching.

## Slide 12: 5. Packet Switching / Store-and-forward
Networking example
R1 doesn't simply send the packet blindly.
It receives the IP packet, determines the next hop, and forwards it.

## Slide 13: 6. Connectionless / Datagram Service
The Network Layer can conceptually provide connectionless service.
In a connectionless network: A connection does not have to be established before sending packets.
IP uses this model.
Suppose: PC1 → R1 → R2 → PC2
PC1 can create an IP packet:
Source IP: 192.168.1.10
Destination IP: 192.168.5.20 and sends it.
There is no requirement that PC1 first establish a dedicated network-layer connection with PC2.
Each IP packet is treated independently.
This is called: Datagram Service

## Slide 14: 6. Connectionless / Datagram Service
For example:
Packet 1 → R1 → R2 → PC2
Packet 2 → R1 → R3 → PC2
Packet 3 → R1 → R2 → PC2
Conceptually, packets can potentially take different paths.
Important clarification This does not mean UDP at the transport layer.
At Transport Layer: UDP -> UDP Datagram. At Network Layer: IP -> IP Packet / IP Datagram. They are different PDUs at different layers.
For example:

## Slide 15: 7. Fragmentation and Reassembly
Different networks can support different maximum packet sizes.
This maximum size is called: MTU (Maximum Transmission Unit)
Suppose: Network A MTU = 1500 bytes
Network B MTU = 500 bytes A Packet of: 1200 bytes can travel through network A. But it cannot fit into a network whose MTU is only 500 bytes. Under IPv4, Fragmentation may be required.
The fragments are eventually reassembled at the destination.
Important IPv4/IPv6 distinction
IPv4: Routers can fragment packets under the IPv4 rules.
IPv6: Routers do not fragment packets in transit. The source must use the IPv6 fragmentation mechanism if fragmentation is necessary.

## Slide 16: 9. Congestion Control / Traffic Management
Now consider this situation:
Suppose the incoming traffic is: 100 Mbps but the outgoing link can only handle 10 Mbps. The router cannot forward everything immediately. At this moment, Packets starts accumulating in its buffer.
This is congestion.

## Slide 17: 9. Congestion Control / Traffic Management
Congestion can cause:
Increased delay
Packet loss
Buffer overflow
Reduced throughput
Retransmissions
Traffic shaping
One way to control the amount/rate of traffic entering the network is traffic shaping.
Two important algorithms are:
Leaky Bucket
Token Bucket

## Slide 18: IP Addressing
Let’s recall the unit 1. Every network interface has a MAC address.
For example: PC1
MAC Address = 00:1A:2B:3C:4D:5E
Ques: If every computer already has a MAC address, why do we need an IP address? This is one of the most important questions in networking. The answer is that MAC addressing and IP addressing solve different problems.

## Slide 19: IP Addressing
MAC Address is a Layer 2 address
MAC addresses belong to the: Data Link Layer — Layer 2
For example: 00:1A:2B:3C:4D:5E
A switch uses MAC addresses to make forwarding decisions inside a Layer 2 network.
Consider: PC1 ───── Switch ───── PC2
PC1 wants to communicate with PC2.
The switch can learn:
and forward an Ethernet frame toward the appropriate port.
So MAC addresses are very useful for local network delivery.
But what happens when the destination is on another network?

## Slide 20: IP Addressing
Now consider:
Suppose: PC1 = 192.168.1.10
PC2 = 192.168.2.10
PC1 and PC2 belong to different IP networks. The packet must travel through a router:
Now ask:
Can PC1 simply use PC2's MAC address to send the packet across the entire network? NO
The MAC address is primarily used for local Layer 2 delivery. Routers operate at Layer 3 and use IP addressing to determine where a packet needs to go.
This is why we need: IP Addressing

## Slide 21: IP Addressing
An IP address is a logical address assigned to a network interface so that devices can be identified and reached at the Network Layer.
For example: 192.168.1.10
Unlike a MAC address, which is associated with the network interface at Layer 2, an IP address is used to identify a device/interface within an IP network and can change when the device moves between networks.
Why is it called a logical address? Eg: Today you connect it to: University Network It might receive: 192.168.10.25 Tomorrow you connect the same laptop to: Home Network It might receive: 192.168.1.15
The laptop's network interface can retain the same MAC address, but its IP address can change according to the network it is connected to.

## Slide 22: IP Addressing
So: MAC Address
↓
Associated with network interface
IP Address
↓
Associated with its location within an IP network This logical structure is extremely important for routing.
IP address is not just "an address of a computer“ This is a subtle but important point.
We often casually say:
"PC1 has IP address 192.168.1.10."
But technically, an IP address is assigned to a network interface.
A router can have multiple interfaces:
For example:
G0/0 → 192.168.1.1
G0/1 → 192.168.2.1
So the router has different IP addresses on different interfaces.
This makes sense because each interface connects to a different network.

## Slide 23: IPv4 and IPV6
There are two major versions of IP: IPV4 and IPV6
IPv4
Internet Protocol version 4
Example:
192.168.1.10
IPv6
Internet Protocol version 6
Example:
2001:db8:abcd:0012::10
IPv4 and IPv6 are both Network Layer protocols.
IPv4 Address — Basic Structure
An IPv4 address is: 32 bits long. For example: 192.168.1.10 looks like four decimal numbers, but internally the computer sees: 11000000.10101000.00000001.00001010
Why are there four numbers?
An IPv4 address contains: 32 bits
These 32 bits are divided into four groups of 8 bits.
Each 8-bit group is called an: OCTET
Therefore:
32 bits
↓
8 + 8 + 8 + 8
↓
4 octets

## Slide 24
Each octet contains 8 bits.
The largest value that 8 bits can represent is: 11111111
In decimal: 128 + 64 + 32 + 16 + 8 + 4 + 2 + 1 = 255
The smallest value is: 00000000 = 0
Therefore, every IPv4 octet can contain: 0 to 255
So: 192.168.1.10 is a valid IP Address, but 192.168.1.300 is not because 300 cannot be represented using 8 bits. Example: 192.168.1.10 Convert each octet into binary: 192 = 11000000 168 = 10101000 1 = 00000001 10 = 00001010 11000000.10101000.00000001.00001010

## Slide 25
The most important concept: Network Part and Host Part
An IP address has two conceptual parts:
The: Network Part identifies which network the device belongs to.
The: Host Part identifies the particular host/interface within that network.
Example
Suppose we have:
192.168.1.10
and assume:
Network = 192.168.1.0 Then conceptually:
So:
192.168.1.10
means conceptually:
"Host 10 on the 192.168.1 network."
But there is an important problem:
How does the router know which bits belong to the network and which belong to the host?
This is where the subnet mask/prefix becomes important.

## Slide 26: Subnet Mask
A subnet mask tells us which portion of an IPv4 address represents the: Network portion and which portion represents the: Host portion
For example:
The mask can also be written as: /24 So, 192.168.1.10/24 means, The first 24 bits represents the network portion.
Understanding /24
Remember: IPV4 = 32 bits If we have, / 24, it means 24 bits -> Network 8 bits -> Host Because: 32 – 24 = 8
In subnetting which we will study later, this thing is very imp.

## Slide 27: Network Address VS Host Address
Let's take: 192.168.10.25/24
The Network is: 192.168.10.0 / 24
The Host is: 25 But there are special addresses within a network. For example: 192.168.10.0 is the Network Address and
192.168.10.255 is the broadcast address for that /24 network.
So typically the usable host addresses are: 192.168.10.1 to 192.168.10.254

## Slide 28: Classful Addressing
IPv4 addresses were divided into different classes. Example: Imagine two organizations.
Organization A needs millions of hosts. Organization B needs 100 hosts only. Giving both organizations the same-size network would waste addresses. So, IPV4 addresses were divided into classes of different sizes.
Class A → Very large networks
Class B → Medium-sized networks
Class C → Smaller networks Class D → Multicast
Class E → Experimental/reserved
This was the original classful addressing system.

## Slide 29: Class - A
Class A was designed for very large networks.
The first octet identifies the class and the remaining address space provides a very large host space.
The traditional range is: 1.0.0.0
to
126.255.255.255 The first octet is: 1 – 126 The default subnet mask is: 255.0.0.0 OR /8 Conceptually: Therefore Class A had: 8 network bits
24 host bits The host portion can theoretically provide: 2^24 addresses per network, though special addresses are reserved.

## Slide 30: Class - A
Why doesn't Class A include 127? The range: 127.0.0.0/8 is reserved for loopback. For example: 127.0.0.1 is commonly used as the IPv4 loopback address. It refers back to the local host rather than being used as an ordinary network destination. Therefore: Class A: 1 – 126 NOT 1 - 127

## Slide 31: Class - A
Its structure is:
Therefore: Network bits = 8
Host bits = 24 But there's something interesting here.
The first bit of a Class A address is fixed as: 0 So the actual structure is:
Therefore: 1 bit → Class identification
7 bits → Network ID
24 bits → Host ID Total: 1 + 7 + 24 = 32

## Slide 32: Class – A - Why does Class A start with 0?
This is where the Class A range comes from. A Class A address must begin with binary 0.
An 8-bit first octet looks like: 0xxxxxxx The remaining 7 bits can be either 0 or 1. Hence, The smallest possible value is: 00000000 Which is 0.
The Largest Possible value is: 01111111 Which is 127.
Therefore, the theoretical first-octet range is: 0 – 127 But not all of it is available for ordinary Class A network assignment.

## Slide 33: Networks Possible in Class A
The first bit is fixed as 0. Therefore, only 7 bits remain for identifying networks. So, 2^7 = 128 network numbers are possible. But 0 and 127 are reserved. Hence, 128 – 2 = 126

## Slide 34: Host Possible in Class A
Class A has: 24 host bits. Therefore, 2^24 possible host combinations. But two addresses have special purposes in a conventional subnet: All Host bits = 0. This represents the: Network Address All Host bits = 1. This represents the: Broadcast Address. Therefore, 2^24 – 2 16,777,216 – 2 = 16,777,214 usable hosts per traditional class A network.

## Slide 35: Class - B
Class B was designed for medium-sized networks. Traditional range: 128.0.0.0
to
191.255.255.255 First octet: 128 – 191 Default subnet mask: 255.255.0.0 OR /16 Conceptually:
Therefore: 16 network bits and 16 host bits The theoretical number of addresses per Class B network is: 2^16=65,536 with two addresses traditionally unavailable for ordinary host assignment in a conventional subnet: Network Address & Broadcast Address. So a conventional /16 network has: 65,536−2=65,534 usable host addresses.

## Slide 36: Class - B
Its structure is:
But the first two bits are used to identify the class. Class B starts with: 10, therefore,
So: 2 bits → Class identification
14 bits → Network ID
16 bits → Host ID Total: 2 + 14 + 16 = 32

## Slide 37: Class – B - Why does Class B start with 10?
The first two bits are fixed: 10 The remaining six bits of the first octet can vary. So the first octet ranges from: 10000000 to 10111111 Minimum: 10000000 = 128 Maximum: 10111111 = 191 Therefore, range is: 128 - 191

## Slide 38: Networks Possible in Class B
We have: 14 bits → Network ID

## Slide 39: Host Possible in Class B
There are: 16 Host bits
1 Network address
1 Broadcast address

## Slide 40: Class - C
Class C was designed for smaller networks. Traditional range: 192.0.0.0
to
223.255.255.255 First octet: 192 – 223 Default subnet mask: 255.255.255.0 OR /24 Conceptually:
So: 24 network bits 8 host bits. Theoretical addresses: 2^8=256 Usable host addresses: 256−2=254 for a conventional /24 subnet.

## Slide 41: Class - C
Class C starts with: 110 Its structure is:
Therefore: 3 bits → Class identification
21 bits → Network ID
8 bits → Host ID Total: 3 + 21 + 8 = 32

## Slide 42: Class – C - Why does Class C start with 110?
The first three bits are fixed: 110 The remaining five bits can vary. Therefore the first octet ranges from: 11000000 to 11011111. Minimum: 11000000 = 192 Maximum: 11011111 = 223 Therefore, range is: 192 - 223

## Slide 43: Networks Possible in Class C
Class C has: 21 Network bits

## Slide 44: Host Possible in Class C
Class C has: 8 Host bits
Network address
Broadcast address

## Slide 45: Class - D
Class D is different. It is used for MULTICAST. Range: 224.0.0.0
to
239.255.255.255 It is not divided into the traditional network/host structure used by Classes A, B and C. For example, multicast allows one sender to communicate with a group of receivers. Conceptually:
Instead of sending three separate transmissions, multicast allows the sender to send to a multicast group.

## Slide 46: Class - E
Class E historically covers: 240.0.0.0
to
255.255.255.255 It was reserved for: Experimental / reserved purposes. It was not intended for ordinary host addressing.

## Slide 47: Classful Addressing
Class | First Octet | Default Mask | Prefix | Purpose
A | 1–126 | 255.0.0.0 | /8 | Very large networks
B | 128–191 | 255.255.0.0 | /16 | Medium-sized networks
C | 192–223 | 255.255.255.0 | /24 | Smaller networks
D | 224–239 | — | — | Multicast
E | 240–255 | — | — | Experimental/reserved

## Slide 48: Practice Questions